1. MPI_Init - Initializes the MPI execution environment

#include <mpi.h>
int MPI_Init(int *argc, char ***argv)
All MPI programs must contain a call to MPI_Init
2. MPI_Comm_size - Returns the size of the group associated with a communicator.
MPI_Comm_size(MPI_COMM_WORLD,&numprocs);
This function indicates the number of processes involved in a communicator. For MPI_COMM_WORLD, it indicates the total number of processes available.
3. MPI_Comm_rank(MPI_COMM_WORLD,&myid);
Determines the rank of the calling process in the communicator.
## Input Parameters
comm
Communicator (handle).
## Output Parameters
rank
Rank of the calling process in group of comm (integer).
IERROR
Fortran only: Error status (integer).
3. MPI_Recv - Performs a standard-mode blocking receive.

int MPI_Recv(void *buf, int count, MPI_Datatype datatype,
    int source, int tag, MPI_Comm comm, MPI_Status *status)
## Input Parameters
count
Maximum number of elements to receive (integer).
datatype
Datatype of each receive buffer entry (handle).
source
Rank of source (integer).
tag
Message tag (integer).
comm
Communicator (handle).
## Output Parameters
buf
Initial address of receive buffer (choice).
status
Status object (status).
IERROR
Fortran only: Error status (integer).
This basic receive operation, MPI_Recv, is blocking: it returns only after the receive buffer contains the newly received message.

MPI_Send - Performs a standard-mode blocking send.
int MPI_Send(const void *buf, int count, MPI_Datatype datatype, int dest,
    int tag, MPI_Comm comm)

Input Parameters
buf
Initial address of send buffer (choice).
count
Number of elements send (nonnegative integer).
datatype
Datatype of each send buffer element (handle).
dest
Rank of destination (integer).
tag
Message tag (integer).
comm
Communicator (handle).
## Output Parameter
IERROR
Fortran only: Error status (integer).
This routine will block until the message is sent to the destination.